## Slide 1: FilterDemod_ref
Documentation for the filterDemod_ref function

## Slide 2: GNU Radio
Open source software tool for digital signal processing and radio control
  Python based – runs best in linux environments
    Run on
      Pentoo (.iso booted from a flashdrive)
      Raspian (OS for raspberry pis)
      Lasso server
      Windows (can do basic functions, but no hardware connection)
Block Diagrams
Synergizes nicely with HackRF hardware
  11-part tutorial available: https://greatscottgadgets.com/sdr/1/

## Slide 3: GNU Radio Setup
Key Linux commands for installation
  sudo apt-get update (if necessary)
  sudo apt-get install hackrf
  sudo apt-get install gnuradio_companion
  sudo apt-get install gr-osmosdr
Commands to see if software works
  hackrf_info
  Gnuradio_companion
GreatScott tutorial has sample programs to test

## Slide 4: filterDemod_ref function
Python executable
Takes a binary data file (complex IQ samples) and puts it through a FIR low pass digital filter and then a wide-band FM receiver (demodulation) to output a .wav file of real data
Does not sacrifice any data samples or time accuracy/resolution
Can filter down to whatever bandwidth is necessary

## Slide 5
filterDemod_ref.grc in GNU Radio Companion

## Slide 6: Options Block
Generate options is set to “NO GUI” because this program does not require a gui
Run options is set to “Run to Completion”
  This will run the program until the file source block stops it

## Slide 7: Parameter Blocks
  samp_rate (int, default = 2000000)
    Must match the rate that the data was sampled at
    Minimum is 2 MSPS (default), maximum is 20 MSPS
  source_file (String, default = “”)
    Sets the local directory for the binary file containing the input data
    Full path is required, including the file name
  save_file (String, default = “”)
    Sets the local directory for the .wav file containing output the data
    Full path is required, including the new file name with “.wav” on the end
  decimation (int, default = 1)
    Enables decimation of samples (divides sample rate)
  gain (int, default = 1)
    Enables a gain for the samples (multiplies each sample by a constant)

## Slide 8: Parameter Blocks
  cutoff_freq (int, default = 80000)
    Defines that highest frequency on either side of the center (f=0) that is allowed to pass through the filter
    Does not remove samples or shrink frequency window in fft
    Ex. Signal is centered at 100 MHz with a signal bandwidth of 160 kHz. A cutoff frequency of 80 kHz will filter out all signals outside of 99.92 MHz – 100.08 MHz
  trans_width (int, default = 2000)
    Determines the steepness of the filter at the cutoff frequency in Hz

## Slide 9: Low Pass Filter Block
Uses a series of weighted delays to achieve a finite impulse response filter
  All delays and coefficients are calculated “behind the scenes” depending on the parameters

## Slide 10: Throttle Block
Throttle blocks are necessary for any “purely software” operations in GNU Radio to prevent overloading of CPU

## Slide 11: WBFM Receive Block
Performs FM demodulation operation on the complex IQ data (blue), resulting in a stream of real data (orange)

## Slide 12
filterDemod_ref.grc in GNU Radio Companion

## Slide 13: Application
This program can be run manually on a local PC or in an automated program that runs on the LASSO server
  filterReader.py is a python executable that calls this program for a structured directory of data

## Slide 14: Notes
There is a detailed How To for running this program on the LASSO server “cross-correlation and automated filtering”
Lines 17 and 44 are commented out of filterDemod_ref.py because of an issue with polymorphic types
  The .grc file generated these lines but they are not necessary and cause errors
  Regeneration of the .py file will bring these lines back, so they must be again commented out each time